## Slide 1: Discussion 1B – Week 7

## Slide 2: Connections

## Slide 3: Things we will discuss
Go over connections.
MRAA library functions.
Grove temperature sensor and an Algorithm to convert the temperature reading.
Commands and the options.

## Slide 4: MRAA library functions
mraa_gpio_context mraa_gpio_init ( int pin )
  Initialise gpio_context, based on board number
  Parameters
    pin Pin number read from the board, i.e IO3 is 3
  Returns
    gpio context or NULL
mraa_result_t mraa_gpio_dir (mraa_gpio_context dev, mraa_gpio_dir_t dir )
  et Gpio direction
  Parameters
    dev The Gpio context
    dir The direction of the Gpio
  Returns
    Result of operation

## Slide 5
int mraa_gpio_read ( mraa_gpio_context dev )
  Read the Gpio value. This can be 0 or 1. A resonse of -1 means that there was a fatal error.
  Parameters
    dev The Gpio context
  Returns
    Result of operation
mraa_result_t mraa_gpio_close(mraa_gpio_context dev)
  Close the Gpio context.
  Will free the memory for the context and unexport the Gpio
  Parameters
    dev The Gpio context
  Returns
    Result of operation

## Slide 6
mraa_aio_context mraa_aio_init ( unsigned int pin
  Initialise an Analog input device, connected to the specified pin
  Parameters
    pin Channel number to read ADC inputs
  Returns
    aio context or NULL
int mraa_aio_read ( mraa_aio_context dev )
  Read the input voltage. By default mraa will shift the raw value up or down to a 10 bit value.
  Parameters
    dev The AIO context
  Returns
    The current input voltage or -1 for error

## Slide 7
mraa_result_t mraa_aio_close ( mraa_aio_context dev )
  Close the analog input context, this will free the memory for the context
  Parameters
    dev The AIO context
  Returns
    Result of operation

## Slide 8: Grove temperature sensor
Should be using mraa_aio_read() instead of analogRead()

## Slide 9: Commands and Options
--scale=C
--period=#
--log=filename
OFF, STOP, START.